## Slide 1: On Capability of Supporting Windowing for Secure LTF
Date: 2021-01-08
Authors:
Name | Affiliations | Address | Phone | Email
Jianhan Liu | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | jianhan.liu@mediatek.com
Thomas Pare |  |  |  | 
Christian Berger | NXP |  |  | 
Hongyuan Zhang |  |  |  | 

## Slide 2: Status on Windowing
Different Tx frequency-domain (FD) windows had been evaluated and proposed to increase the security of LTF
  Rectangular window [1]
  Raised-cosine (RC) window [2]
  Flat Top window[3]
The following straw poll has been conducted in [3]:
  Do you agree that ISTA/RSTA support following frequency domain windowing?
    Default is Rectangular window (equivalent to no windowing)
    Flat Top window is optional, but recommended for improved security
      Transmitting STA will indicate to receiving STA whether flat top window is used
      Signaling method TBD
    No test for ISTA/RSTA Tx window defined in 11az spec

## Slide 3: Adding capability of Supporting Windowing
Given the Flat Top window is optional, capability of supporting Flat Top window or not shall be indicated at the TX and RX.
  Since Flat Top window is optional, TX and RX should have the freedom to implement it or not implement it.
  A receiver that does not support Flat Top window can avoid potential performance loss caused by TX sending it the secure LTF with Flat Top window.
  A transmitter that does not support Flat Top window can avoid the receiver to sending it request of adding with Flat Top window.

## Slide 4: Straw Poll #1
Do you agree to add the transmit and receive capability of supporting Flat Top window on Secure LTF?

## Slide 5: References
[1] 802.11-20/0836r0, 11az Secure LTF Design
[2] 802.11-20/1855r0, Further Updated on 11az Secure LTF Design
[3] 802.11-20/1595r2, Tx FD Window Design for Secure LTF