## Slide 1: Feasibility of supporting AMP IoT devices in WLAN
Date: 2022-07-08
Authors:
Name | Affiliation | Address | Phone | Email
Chuanfeng He | OPPO |  |  | 
Shengjiang Cui |  |  |  | 
Weijie Xu |  |  |  | xuweijie@oppo.com
Lei Huang |  |  |  | 
Zhisong Zuo |  |  |  | 
Rongyi Hu |  |  |  | 
Zhi Zhang |  |  |  | 
Doc.: IEEE 802.11-22/970r0
July 2022

## Slide 2: Outline
Link budget for different AMP IoT device types
Constraint from energy harvesting
Data rate
Coexistence
Summary
Reference
July 2022
Doc.: IEEE 802.11-22/970r0

## Slide 3: Link budget for different AMP IoT device types (1)
Link budget for AMP-only IoT device with backscatter transmitter
  Three cases are evaluated: case1/2 (energy harvested from radio waves) and case 3 (energy harvested from light).
July 2022
Doc.: IEEE 802.11-22/970r0
 | Case1 | Case2 | Case3
Frequency (MHz) | 920 | 920 | 920
EIRP of AP (dBm) | 30 | 30 | 30
Receiver sensitivity of AP (dBm) | -95 (Note 1) | -95 | -95
Antenna gain of IoT device (dBi) | 2 | 2 | 2
Minimum receiving power for IoT device (dBm) | -20 (Note 2) | -30 (Note 3) | -45 (Note 4)
Maximum communication distance from AP to IoT device (m) | 10.33 | 32.67 | 183.71
Backscattering loss at IoT device (dB) | 5 | 5 | 5
Low Noise Amplifier factor (dB) | 0 | 0 | 30 (Note 3)
Maximum communication distance from IoT device to AP (m) | 103.31 | 32.67 | 183.71
*Notes: Reuse the receiver sensitivity of 802.11 ah AP The minimum required signal power for an IoT device is -20dBm when the IoT device can’t store power itself. It can be -30dBm when the IoT device has the capability of power storage. -45 dBm is assumed as the sensitivity of ultra-low power receiver [1][2][3]. LNA with 30 dBm gain is assumed to boost the backscattering signal, it can have ultra-low power consumption [4][5]. |  |  | 

## Slide 4: Link budget for different AMP IoT device types (2)
Link budget for AMP-only IoT device with active transmitter
July 2022
Doc.: IEEE 802.11-22/970r0
 | Case4
Frequency (MHz) | 920
EIRP of AP (dBm) | 30
Receiver sensitivity of AP (dBm) | -95
Antenna gain of IoT device (dBi) | 2
Minimum receiving power for IoT device (dBm) | -45
Maximum communication distance from AP to IoT device (m) | 183.71
Maximum transmission power of IoT device (dBm) | -15(Note 1)
Maximum communication distance from IoT device to AP (m) | 259.49
*Notes: Ultra-low power active transmitter is assumed[6][7][8]. | 

## Slide 5: Constraints from energy harvesting
July 2022
Doc.: IEEE 802.11-22/970r0
Table 1. Energy harvesting sources [9] [10].
  It can be observed the output power harvested from various power sources is very limited, e.g. from 1uW to 100mW(per cm2/cm3).
  Due to small form factor of AMP-only IoT device, it is required to support maximum power consumption of around 1mW.
  The typical power from ambient power source is summarized as in following table1:
Energy source | Type | Typical power
Outdoor solar light | Natural | 100 mW/cm2 (outdoor),
Indoor office light | Artificial/natural | 100 μW/cm2 (artificial light)–10 mW/cm2 (filtered solar light)
Radio frequency | Artificial | 1uw~100uw
Thermoelectric | Artificial | 60 μW/cm2
Vibration | Artificial | 4 μW/cm3 (human motion) 800 μW/cm3 (machines)
Ambient airflow | Natural/artificial | 1 mW/cm2
Acoustic noise | Natural/artificial | 960 nW/cm3

## Slide 6: Data rate
  For AMP-only IoT device, narrow bandwidth is assumed for data transmission:
    31.25kHz*N for 1 MHz and 2 MHz channel in Sub 1GHz, N = 2,4,8 etc.
    312.5kHz*N for 20 MHz channel in 2.4 GHz (if supported), N = 2,4,8 etc.
  Encoding Rate
    R=1/2,1/4
  Note 1: 20% Guard interval duration in a symbol duration
July 2022
Doc.: IEEE 802.11-22/970r0
Band/Channel | S1G/1M | S1G/2M | S1G/1M | S1G/2M | 2.4G/20M | 
Signal Bandwidth | 31.25kHz*2 | 31.25kHz*8 | 31.25kHz*2 | 31.25kHz*4 | 312.5kHz*2 | 312.5kHz
Symbol Duration | 20 μs | 5 μs | 20 μs | 10 μs | 2 μs | 4 μs
Equivalent Information Bit Duration | 40 μs | 10 μs | 80 μs | 40 μs | 4 μs | 16 μs
R | 1/2 | 1/2 | 1/4 | 1/4 | 1/2 | 1/4
Data rate | 25kb/s | 100kb/s | 12.5kb/s | 25kb/s | 250kb/s | 62.5kb/s

## Slide 7: Coexistence (1)
  Potential AMP PPDU format can be introduced to facilitate backward compatibility.
    For AMP-only IoT devices operating in Sub 1GHz
      AMP PPDU format contains 802.11ah preamble (e.g. including LTF, STF, SIG portion), followed by AMP portion.
    For AMP-only IoT devices operating in 2.4GHz
      AMP PPDU format contains legacy preamble (e.g. L-STF, L-LTF, L-SIG, followed by AMP portion.
    The transmission bandwidth of AMP specific fields can be narrower than that of the preamble. Simple waveform will be adopted for AMP portion.
    example AMP PPDU format
July 2022
Doc.: IEEE 802.11-22/970r0

## Slide 8: Coexistence (2)
  It would be a challenge for AMP-only IoT device to generate the preamble due to required OFDM waveform.
  Backscattering can be one option to tackle the preamble transmission issue.
    AMP-only IoT device backscatters the preamble, which is provided by the AP
    Immediately after the preamble, the AMP-only IoT device transmits the AMP portion. Therefore, as a whole the proposed AMP PPDU format can be transmitted by the AMP-only IoT device.
July 2022
Doc.: IEEE 802.11-22/970r0

## Slide 9: Coexistence (3)
  It may be difficult for an AMP-only IoT device to perform channel access due to its ultra-low power and low complexity receiver
    May not be able to perform CCA and set the NAV
    May not be able to support EDCA protocol
  Triggered UL access mechanism can be used for AMP-only IoT device for UL transmission.
    AP may transmit a Trigger frame to an AMP-only IoT device to solicit UL transmission
July 2022
Doc.: IEEE 802.11-22/970r0

## Slide 10: Summary
  This presentation discusses the feasibility of supporting AMP IoT devices in WLAN, focusing on the following aspects
  Link budget for different AMP IoT device types
  Constraint from energy harvesting
  Data rate
  Coexistence
  Based on the discussion, it can be seen that although there is power constraint from energy harvesting, requirements such as the communication distance, power consumption and data rata etc. can be fulfilled by using ultra-low power backscattering transmitter (or ultra-low power active transmitter ) and ultra-low power receiver.
July 2022
Doc.: IEEE 802.11-22/970r0

## Slide 11: Reference
  J. Im, H. -S. Kim and D. D. Wentzloff, "A 470µW −92.5dBm OOK/FSK Receiver for IEEE 802.11 WiFi LP-WUR," ESSCIRC 2018 - IEEE 44th European Solid State Circuits Conference (ESSCIRC), 2018, pp. 302-305, doi: 10.1109/ESSCIRC.2018.8494331.
  J. Im, H. Kim and D. D. Wentzloff, "A 217µW −82dBm IEEE 802.11 Wi-Fi LP-WUR using a 3rd- Harmonic Passive Mixer," 2018 IEEE Radio Frequency Integrated Circuits Symposium (RFIC), 2018, pp. 172-175, doi: 10.1109/RFIC.2018.8428988.
  R. Liu et al., "An 802.11ba-Based Wake-Up Radio Receiver With Wi-Fi Transceiver Integration," in IEEE Journal of Solid-State Circuits, vol. 55, no. 5, pp. 1151-1164, July 2020, doi: 10.1109/JSSC.2019.2957651.
  J. Kimionis, A. Georgiadis, Sangkil Kim, A. Collado, K. Niotaki and M. M. Tentzeris, "An enhanced-range RFID tag using an ambient energy powered reflection amplifier," 2014 IEEE MTT-S International Microwave Symposium (IMS2014), 2014, pp. 1-4, doi: 10.1109/MWSYM.2014.6848653.
  D Matos, R Correia,NB Carvalho, ”Dual-Band FET-Based Reflection Amplifier for Backscatter Modulator Performance Enhancement” URSI Radio Science Letters, 2021
  K. Tang et al., "A 75.3 pJ/b Ultra-Low Power MEMS-Based FSK Transmitter in ISM-915 MHz Band for Pico-IoT Applications," 2021 IEEE International Symposium on Circuits and Systems (ISCAS), 2021, pp. 1-4, doi: 10.1109/ISCAS51556.2021.9401715
  M. S. Jahan, J. Langford and J. Holleman, "A low-power FSK/OOK transmitter for 915 MHz ISM band," 2015 IEEE Radio Frequency Integrated Circuits Symposium (RFIC), 2015, pp. 163-166, doi: 10.1109/RFIC.2015.7337730.
  J. Bae and H. Yoo, "A low energy injection-locked FSK transceiver with frequency-to-amplitude conversion for body sensor applications," 2010 Symposium on VLSI Circuits, 2010, pp. 133-134, doi: 10.1109/VLSIC.2010.5560325.
  N. Dang, E. Bozorgzadeh and N. Venkatasubramanian, "Chapter 6 -Energy Harvesting for Sustainable Smart Spaces" in Advances in Computers., Elsevier, vol. 87, pp. 203-251, 2012.
  Energy harvesting technologies[M]. New York: Springer, 2009.
July 2022
Doc.: IEEE 802.11-22/970r0